## Slide 1
Scenario 12: Loading Unit Geo-Fence Characteristics
Version October 2020
Vehicle Interaction Control Improvement Project
Vehicle Interaction Knowledge Hub Resource - Story Board Series

## Slide 2: Adapting and Using EMESRT Story Boards
What are they?
The Story Board approach was developed by an EMESRT Member Company to assist with the specification and installation of Proximity Detection Systems (PDS) on mobile equipment at surface mines
They provide a visual and dynamic reference for equipment operators, PDS suppliers VI Control Improvement project managers as they implement VI intervention controls (EMESRT Levels 8–9)
How can I use them?
Review each Story Board in presentation mode
As required, adapt the resource to your circumstances
Use the Story Boards as a resource during Phase 4 - New Technology Implementation
Remember LO = Local Object and RO = Remote Object (reference EMERST PR5A)

## Slide 3
50 meters
Definitions
LUG – Loading Unit Geo-fence
HT – Haul Truck
Configurable Parameters
  Geo-fence activates @ speeds <X kph
  LUG diameter configurable (in meters)
  Normal CAS restored and LUG inactive @ speeds >X kph
LUG alarm logic disabled between Loading Unit and specified equipment:
  Dozer
  HT when HT speed is <Y kph
Dozer Parameters
  Should normal CAS alarm logic not be proven (i.e. dozer produces excessive nuisance alarms during close interactions with HT) then the outer beam on dozer is to have the ability to be disabled whilst the dozer is inside the LUG
Normal Loading Procedure “No Alarms”
Loading Unit Geo-Fence Characteristics