## Slide 1
VEHICLE INTERACTION CONTROL IMPROVEMENT
Surface Functional Performance Scenario Storyboards

## Slide 2
Adapting and Using the Storyboards
What are scenario storyboards?
The Functional Performance Scenario Storyboard approach was developed by an EMESRT Member Company to better understand the fatal vehicle interaction scenarios in a surface mine and to then compare the capability of vehicle interaction technologies to mitigate or eliminate the exposures detailed in the storyboards. This has enabled designers to better develop and install vehicle interaction technologies appropriate mobile equipment interactions at surface mines and recently adapted for Underground mines
They provide a visual and dynamic reference for equipment operators, technology suppliers, Vehicle Interaction Control Improvement project managers as they implement vehicle interaction intervention controls (EMESRT Levels 7, 8 and 9)
How can I use the scenario storyboards?
Once downloaded, review each Storyboard in presentation mode
Use the Storyboards as a resource during Phase 4 – Vehicle Interaction Control Enhancement
As required, apply the specific scenario storyboards in your functional performance environment context to derive the configuration settings
Generally, in the storyboards these definitions apply:
LO = Local Object (causing the interaction)
RO = Remote Object (affected by the interaction)

## Slide 3: User interface behaviour – vehicle to vehicle interaction
NOTE: the text in red provides examples of parameters that should be considered during development and site configuration.
Nil Interaction
No VI event audibles
No detection beams visible
Alert
Occurs when outer to outer or inner to outer/outer to inner beams on two vehicles intersect
User interface zooms to the interaction
Detection beams on both vehicles turn yellow then red
Default audible message of “Alert” is activated, definitive audibles used for specific VI scenarios
Audible played twice then a 3 second gap and repeated until situation rectified
Audible played at 5 dB above ambient noise
Alarm
Occurs when inner beam intersects with inner beam or body of another vehicle
User interface remains bright and zoomed to the interaction
Detection beams on both vehicles remain red
Default audible of “Shrill”, “Stop”, definitive audibles used for specific VI scenarios
Audible without the “Shrill” repeated with 1.5 second gap until situation rectified
Audible played at 10 dB above ambient noise

## Slide 4
LO (LV) approaches a formal T-intersection configured with an intersection geo-fence
When the inner beam of the LO (LV) enters the geo-fenced intersection (30 m from intersection) CAS will scan for other CAS units that are located within the geo-fence
The geo-fence will have a speed limit of 40 km/h applied and will be activate when LV’s and MV’s enter regardless of the presence of an RO
If T-intersection geo-fence becomes occupied by the body of any other vehicle whilst the LO (LV) is in the intersection the following will occur:
  User interface will brighten in LO and RO’s
  Audible message of “Give Way” repeated twice will only activate in LV designated vehicles not in HV’s
If the LO (HV or LV) becomes the only vehicle inside the geo-fenced intersection or departs the geo-fenced intersection the user interface will then dim
Audible message will activate once only per entry into geo-fence
Applicable for LV’s and MVs when they are the LO.
Not applicable for dozers, drills and tracked loading units when they are the RO.
30 m
30 m
NOTE: the text in red provides examples of parameters that should be considered during development and site configuration.
Scenario 4: T-intersections – light vehicle perspective