## Slide 1
VEHICLE INTERACTION CONTROL IMPROVEMENT
Surface Functional Performance Scenario Storyboards

## Slide 2
Adapting and Using the Storyboards
How can I use the scenario storyboards?
Once downloaded, review each Storyboard in presentation mode
Use the Storyboards as a resource during Phase 4 – Vehicle Interaction Control Enhancement
As required, apply the specific scenario storyboards in your functional performance environment context to derive the configuration settings
What are scenario storyboards?
The Functional Performance Scenario Storyboard approach was developed by an EMESRT Member Company to better understand the fatal vehicle interaction scenarios in a surface mine and to then compare the capability of vehicle interaction technologies to mitigate or eliminate the exposures detailed in the storyboards. This has enabled designers to better develop and install vehicle interaction technologies appropriate mobile equipment interactions at surface mines and recently adapted for Underground mines
They provide a visual and dynamic reference for equipment operators, technology suppliers, VI Control Improvement project managers as they implement VI intervention controls (EMESRT Levels 7, 8 and 9)

## Slide 3: User interface behaviour – vehicle to vehicle interaction
NOTE: the text in red provides examples of parameters that should be considered during development and site configuration.
Nil Interaction
No VI event audibles
No detection beams visible
Alert
Occurs when outer to outer or inner to outer/outer to inner beams on two vehicles intersect
User interface zooms to the interaction
Detection beams on both vehicles turn yellow then red
Default audible message of “Alert” is activated, definitive audibles used for specific VI scenarios
Audible played twice then a 3 second gap and repeated until situation rectified
Audible played at 5 dB above ambient noise
Alarm
Occurs when inner beam intersects with inner beam or body of another vehicle
User interface remains bright and zoomed to the interaction
Detection beams on both vehicles remain red
Default audible of “Shrill”, “Stop”, definitive audibles used for specific VI scenarios
Audible without the “Shrill” repeated with 1.5 second gap until situation rectified
Audible played at 10 dB above ambient noise

## Slide 4
Vehicle operator needs to enter within 30 m of HV to access HV
LV operator needs to perform the following once in range of HV (300 m V2X)
  Operator touches the specific HV icon on the user interface
  Selects the “Access” button
HV user screen brightens and receives audible message “Access Request”
  “Accept” or “Reject” Button appears on user interface
  Message appears on user interface “LV ID # would like to access your vehicle”
  HV cannot press the “Accept” button until safe state is achieved, “Reject” button can be pressed
HV engages safe state controls, if not already
  Yellow safe state broadcast to all vehicles in range
HV authorises LV to gain access by pressing “Accept” button
  Green safe state broadcast only to authorised LV
User interface displays a graphical representation in both vehicles, LV is now authorised to enter zone (relevant for that interaction only)
If any condition of safe state is broken during accessing, approval on both vehicles is void and an event is triggered with an audible message of “Breach” on the LV and “Don’t Move” on the HV
Only applicable for LV’s, MV’s and Fuel Trucks to all HV’s (excludes LV’s & MV’s to LV’s & MV’s)
30 metre zone must be visible on all user panels at all times when the vehicle is stationary (red), in a safe state (yellow). An acknowledged safe state (green) will only be visible to the two vehicles that are interacting.
Accept
LV #1 DESIRES ACCESS
LO = LV
O Kph
Neutral
Brake Set
PASS
ACCESS
RO = HV
REJECT
NOTE: the text in red provides examples of parameters that should be considered during development and site configuration.
Scenario 7B: Accessing heavy vehicle – maintenance activities