## Slide 1
VEHICLE INTERACTION CONTROL IMPROVEMENT
Surface Functional Performance Scenario Storyboards

## Slide 2
Adapting and Using the Storyboards
How can I use the scenario storyboards?
Once downloaded, review each Storyboard in presentation mode
Use the Storyboards as a resource during Phase 4 – Vehicle Interaction Control Enhancement
As required, apply the specific scenario storyboards in your functional performance environment context to derive the configuration settings
What are scenario storyboards?
The Functional Performance Scenario Storyboard approach was developed by an EMESRT Member Company to better understand the fatal vehicle interaction scenarios in a surface mine and to then compare the capability of vehicle interaction technologies to mitigate or eliminate the exposures detailed in the storyboards. This has enabled designers to better develop and install vehicle interaction technologies appropriate mobile equipment interactions at surface mines and recently adapted for Underground mines
They provide a visual and dynamic reference for equipment operators, technology suppliers, VI Control Improvement project managers as they implement VI intervention controls (EMESRT Levels 7, 8 and 9)

## Slide 3: User interface behaviour – vehicle to vehicle interaction
NOTE: the text in red provides examples of parameters that should be considered during development and site configuration.
Nil Interaction
No VI event audibles
No detection beams visible
Alert
Occurs when outer to outer or inner to outer/outer to inner beams on two vehicles intersect
User interface zooms to the interaction
Detection beams on both vehicles turn yellow then red
Default audible message of “Alert” is activated, definitive audibles used for specific VI scenarios
Audible played twice then a 3 second gap and repeated until situation rectified
Audible played at 5 dB above ambient noise
Alarm
Occurs when inner beam intersects with inner beam or body of another vehicle
User interface remains bright and zoomed to the interaction
Detection beams on both vehicles remain red
Default audible of “Shrill”, “Stop”, definitive audibles used for specific VI scenarios
Audible without the “Shrill” repeated with 1.5 second gap until situation rectified
Audible played at 10 dB above ambient noise

## Slide 4
NOTE: the text in red provides examples of parameters that should be considered during development and site configuration.
LV operator needs to enter within 30 m of HV
LV operator attempts two-way radio contact with HV with no response
HV is parked in a safe area and the ladder is down
HV has safe state controls engaged:
  Zero speed
  Gear to neutral
  Park brake set
  Ladder is down
  Or the vehicle is fully isolated
Safe state is broadcast to all CAS systems. LV makes request to access unmanned vehicle and must wait 15 seconds for possible approval from operator before system auto approves request. Requests for passing are auto approved after 5 seconds
Only applicable for LV’s, MV’s and Fuel Trucks to all HV’s (excludes LV’s & MV’s to LV’s & MV’s).
30 metre zone must be visible on all user panels at all times when the vehicle is stationary (red), in a safe state (yellow). An acknowledged safe state (green) will only be visible to the two vehicles that are interacting.
LO = LV RO = HV
Scenario 7D: Accessing stationary heavy vehicle – assumed un-manned